## Slide 1: Water Prism: Decision Support Framework for Water Resource Risk Management
Robert Goldstein Senior Technical Executive, Water & Ecosystems
WSWC–WGA Energy–Water Nexus Workshop Denver, April 2, 2013

## Slide 2: Approaches to Reaching Sustainability
Top down
  Community/region/watershed-based
  Considers all stakeholder demands
  Matches aggregate water demands to supply
Bottom up
  Sector/Facility-based
  Objectives
    Increase water use efficiency
    Conservation

## Slide 3: Drivers for Development of Water Prism
Electric power generators reliance on water resources
Manage environmental, regulatory, reputational, and financial risks
Water stewardship disclosure requests
Water saving technologies are emerging for all sectors
A need for tools to evaluate strategies across sectors:
  Accommodate future demands within limits of available water
  Encourage collaborative water planning
Roadmap for sustainability is difficult to define given system complexities
Evaluate benefits of water resource management strategies and technologies

## Slide 4: Water Prism Conceptual Design
Examine various scenarios to consider water use reductions needed to keep “demand” below “supply”
Compute system water balance on regional scale
  Surficial watershed model
  Groundwater sources and uses
Project consumptive and withdrawal demands for 40 to 50 year horizon
Explore water saving strategies through scenario analysis
Water Prism Volume 1: Tool Development (EPRI 1023771)

## Slide 5: Water Prism Design Overview
Groundwater
Storage
Land use, Climate, Topography, etc.
Population, Energy Demand, Irrigated Land use
Available Surface Water
Watershed Model
Water Prism Access Database
Water Prism DSS
Ground Water Data

## Slide 6: Four Basic Steps of a Water Prism Analysis
Add Water User Inputs
Review System Water Balance
Build Water Prism Scenarios
Display Water Prism Results
Define Available Surface Water (calibrate watershed model)
Define Available Groundwater (map and parameterize major aquifers)
Major Water Prism Steps
1. Calculate regional water balance
2. Compare projected water demand with available water
3. Generate scenarios with water saving strategies
4. Display reduced water consumption and/or withdrawal as a Water Prism spectrum

## Slide 7: Preliminary Water Prism Applications
2. Green River Watershed
1. Muskingum River Watershed
Goal – demonstrate tool functionality
Leverage watershed modeling from EPRI’s Water Quality Trading Project
Promote synergies between projects

## Slide 8: Muskingum Watershed Background
Area: ~8,000 mi2
  Spans 5 counties and sections of 22 others
  Several cities
  Largely agriculture
Water Use:
  174 surface water withdrawals
  329 groundwater withdrawals
  319 point sources
Power Plants:
  2 large coal-fired – primarily once-through cooling
  2 small coal-fired
  3 NGCC (1 going online 2012) closed cycle cooling
Notes: Akron and Canton are major cities in the NE portion of the watershed. Columbus lies to the west of the shed.

## Slide 9: Muskingum River Power Plants
Power Plants in the Muskingum River Basin |  |  |  |  | 
Plant | Type | Owner | Capacity (MW) | Cooling Technology | Water Source
Conesville | Coal-fired | AEP | 1745 | once-through(1 unit)/ closed cycle (3 units) | Muskingum River, some groundwater
Muskingum | Coal-fired | AEP | 1425 | once-through (4 units)/ closed cycle (1 unit) | Muskingum River, some groundwater
Waterford | Natural Gas (CC) | AEP | 917 | closed cycle | surface water
Dresden* | Natural Gas (CC) | AEP | 580 | closed cycle | surface water
Washington | Natural Gas (CC) | Duke | 620 | closed cycle | surface water
Dover | Coal-fired, Natural Gas | City of Dover, OH | 36.5 | once-through (1 unit), closed cycle (2 units) | surface water, some groundwater
Orrville | Coal-fired | Orrville Dept. of Public Utilities | 84.5 | closed cycle | wastewater effluent, some municipal and groundwater
* Under construction; expected to go on line in 2012 |  |  |  |  | 

## Slide 10: Input Data Sets for WARMF and Water Prism
Required Data Sets | Watershed Model (WARMF) | Water Prism DSS | Data Source | Time Period | Frequency
Topography (DEM) |  |  | USGS NED | 2009 | 30 meter
Land use / land cover |  |  | NLCD | 2006 | N.A.
Climate |  |  | NCDC | 1990-2009 | Daily
Observed streamflow |  |  | USGS | 1990-2009 | Daily
Groundwater properties (aquifers, recharge) |  |  | USGS | N.A. | N.A.
Ecological flow / reservoir limits |  |  | ? | ? | ?
Water withdrawals |  |  | ODNR | 1990-2009 | Monthly
Water discharges |  |  | OEPA | 1990-2009 | Daily
Projected demands (electric power) |  |  | AEP | Through 2014 | N.A.
Projected demands (other sectors) |  |  | Dziegielewski et. al, 2004 | 2005-2025 | 5-Year
Notes: NLCD 2006 is the most recent land cover. Water withdrawals were provided in terms of a monthly volume. This was converted to a daily flowrate (constant for each month). Dziegielewski from Southern Illinois University, Department of Geography

## Slide 11: Land Use / Land Cover (2006 NLCD)
Notes: Mainly rural, deciduous followed by corn/soybean

## Slide 12: Principal Aquifers
4 Principal Aquifers
  389 to 3741 mi2
Unconsolidated
  Shallow, follows river valleys, high porosity, high yield
Bedrock
  Deeper, low porosity, low yield
Notes: Four principal aquifers. Cross-hatched is bedrock, deep, unproductive. Coarse grained near rivers has higher porosity, more productive. A lot of groundwater withdrawals there. Will treat as 4 control volumes, using thickness and porosity to track recharge.

## Slide 13: Withdrawals and Returns
Surface water withdrawals
  174 facilities
  789 MGD (2009)
Groundwater withdrawals
  329 facilities
  131 MGD (2009)
Point source discharges
  319 stations at 307 facilities
  915 MGD (2009)
Notes: 789 + 131 = 920 > 915. 5 MGD consumed in 2009

## Slide 14: Development of Water Prism Strategies
Planned power plant changes
  Retiring once-through coal units
  Conversion of coal to natural gas combined-cycle (NGCC)
  New NGCC plant on-line
Reduction in municipal and industrial
  BAU: State of Ohio projects increased water use due to increased population, increased per capita use and growth in industrial sector
  Prism Strategy: Assume decreased per capita use
    Reduce withdrawals and returns for municipal and industrial users
    8% to 25% reduction over 60 year period

## Slide 15: Water Prism Scenario: Reduced Per Capita Use
Surface Water – Small Tributary
Reduced Consumptive Demand for Each Sector
Savings from Each Sector

## Slide 16: Water Prism Illustrates Impact of Decommissioning and Gas Conversion

## Slide 17: Concluding Thoughts
There is no such thing as Business as Usual - everything is evolving with time
Everything is geographically distributed non-uniformly
Top down management is necessary for sustainability
  Need localized, fine resolution decision support tool to manage community (watershed, region) water resources
  Strategic and technological approaches depend on location
  Research can lead to promising breakthrough technologies to save water