## Slide 1
The Importance of Groundwater in Sustaining Streamflow in the Upper Colorado River Basin
Matthew Miller
Susan Buto, David Susong, Christine Rumsey, John Solder
U.S. Geological Survey, Utah and Nevada Water Science Centers
May 5th, 2016

## Slide 2
USGS National Water Census:
Colorado River Basin Focus Area Study
Evapotranspiration
Snowpack Hydrodynamics
Water Use Information
Groundwater Discharge to Streams
Summarized in Bruce and others (2015) – USGS Fact Sheet 2015-3080

## Slide 3
Project Development and Coordination
Objectives developed from a USGS meeting with selected stakeholders including Reclamation
Strategy focused on filling in information gaps
Lack of groundwater information in UCRB
Groundwater and surface water
are an interconnected resource
Wealth of historic USGS data

## Slide 4
BOR Colorado River Basin Supply and Demand Study
Projected demand is greater than projected supply
Median imbalance of ~ 3.2 million acre-feet by 2060
US Bureau of Reclamation (2012)
Overarching Objective Provide quantitative information that adds new understanding of the joint groundwater-surface water resource in the UCRB

## Slide 5
Study Objectives
Determine the spatial distribution of groundwater discharge to streams (where)
Quantify the fraction of total streamflow that is supported by groundwater discharge (how much)
Quantify the age of groundwater in the UCRB (vulnerability)
USGS
USGS

## Slide 6
Information from streamflow and chemical composition used to separate streamflow into runoff and groundwater components
Chemical Hydrograph Separation
Miller and others (2014, Water Resources Research)

## Slide 7: USGS Long Term Records
Long-term discharge and specific conductance data collected by USGS were used for hydrograph separation.
Data from 1984-2012 used for present study
1947
2010

## Slide 8: Groundwater Discharge to Streams
Miller and others (2014, Water Resources Research)
Hydrograph separation results for Colorado River at Cisco, UT
Summary of 12 Stations in UCRB
“Pulse” of groundwater during snowmelt
Percent of total flow that is groundwater
  Annual: 21 – 58%
  Snowmelt: 13 – 45%
  Low-flow: 40 – 86%

## Slide 9: Discrete data Continuous Data
Problem: Given a small number of observed SC concentration values, and a continuous record of discharge how can we “fill in the gaps” in the SC record?
[
Discharge
Time
Season

## Slide 10: Groundwater Discharge to Streams – Estimation with Discrete Data
Excellent fit between groundwater discharge to streams estimated using measured data and a regression approach at sites not directly impacted by anthropogenic activities
Groundwater discharge to streams estimated at 229 sites using regression approach (sites filtered to remove those directly impacted by anthropogenic activities)
Rumsey et al. (2015, J. Hydrol. – Reg. Stud.)
Miller et al. (2015, J. Hydrol.)

## Slide 11
Developed to estimate long-term mean steady state water quality conditions
USGS SPARROW Model

## Slide 12
Most groundwater discharge to streams occurs in upper elevation catchments
Climate change in high elevation systems will affect the groundwater resource, and therefore the amount of surface water in streams
14.5 maf/yr = Groundwater discharge to streams in Upper Basin
2.7maf/yr = Water delivered to the Lower Basin that originated as groundwater
Water lost during in-stream transport due largely to irrigation withdrawals and evapotranspiration
Spatial Distribution of Groundwater Discharge
Miller and others (in press, Water Resources Research)

## Slide 13
Groundwater and Surface Water – A Single Resource
Mill Creek Near Moab, UT (79% GWD)
Colorado River Near Cisco, UT (55% GWD)
Yampa River at Steamboat Springs, CO (34% GWD)

## Slide 14
On average 56% of streamflow in the UCRB is estimated to be from groundwater discharge
Streamflow in lower elevation catchments is more dependent on groundwater discharge than high elevation systems
These streams support ecologically sensitive habitats (e.g. riparian zones)
Streamflow Sustained by Groundwater
Miller and others (in press, Water Resources Research)

## Slide 15
Age of Groundwater in UCRB
20% of groundwater < 10 years old
65% < 100 years old
Relatively young age of groundwater suggests potential rapid response to changes in environmental conditions
Age Tracers – 3H, Noble gases, CFCs, SF6, 14C

## Slide 16
Summary and Implications
Any processes that affect the groundwater resource will also affect the surface water resource – Now have quantitative estimates of groundwater discharge to streams
Most groundwater discharge to streams occurs in upper elevation watersheds
Streamflow in lower elevation systems is dependent on groundwater discharge to streams
Most groundwater is young, suggesting the potential for rapid response of groundwater discharge to environmental change
Collaborating with Reclamation on study that will use this model as a tool to predict future groundwater discharge to streams under different climate scenarios

## Slide 17
Matt Miller
USGS, Utah Water Science Center
mamiller@usgs.gov
Thank you