## Slide 1
NICE Net and Reference Evapotranspiration in Nevada
Justin Huntington, Dan McEvoy, Greg McCurdy, and Brad Lyles:
Desert Research Institute and Western Regional Climate Center
Irrigation Management Information Systems’ Workshop
August 25-26, San Diego CA
Bridgeport, CA
February, 2015
Snake Valley, NV
October, 2014

## Slide 2
General need for Reference ET (ETo) in NV and elsewhere
Important for estimating ag. consumptive use
Successful application of traditional ETo * Kc approach relies on well watered ETo estimates
METRIC and other remote sensing approaches rely on well watered reference ETo estimates too
NV specific:
  Huge spatial variability in weather
  Each valley has unique weather and deserves own monitoring
  Most groundwater basins are fully or over appropriated due to water rights for irrigation
  Need reliable ETo estimates to calculate crop consumptive use using traditional and remote sensing methods!!
[Allen et al. 1998]

## Slide 3
NICE Net Motivation
Prior to the Nevada Integrated Climate and Evapotranspiration Network (NICE Net) only two NV ag stations
Most NV stations located in dry, non-irrigated environments
Funded by a federal initiative and state of NV to improve estimates of consumptive use in NV
Project started 2010, most stations installed 2010-2012
Fallon AgriMet
Eureka AgriMet

## Slide 4
NICE Net stations
http://nicenet.dri.edu/
Currently 18 NICE Net stations

## Slide 5
NICE Net stations
http://nicenet.dri.edu/
Also hosted on USBR AgriMet page: http://www.usbr.gov/pn/agrimet/agrimetmap/agrimap.html
Big thanks to Jama Hamel!

## Slide 6
NICE Net stations
Carson Valley
Mason Valley
Paradise Valley
Pahranagat Valley

## Slide 7
NICE Net stations
Smith Valley, NV
February, 2015
Precipitation measurements are just as important as ETo!
Needed for net irrigation water requirements
All NICE Net stations now have tipping bucket and weighing type rain gauges
Weighing type gauges are essential for accurate measurement of frozen precipitation
Tipping bucket
Geonor weighing gauge
with Alter shield
Storage gauge to collect
precip isotopes

## Slide 8
NICE Net stations
Sensor list:
CR 1000 data loggers
Campbell HMP45C temperature and humidity sensors
Campbell CS106 barometric pressure sensors
Apogee CS300 pyranometer
R.M. Young 05103 wind speed and direction sensors
Modified Universal precipitation gauge
Texas Electronics TE525 tipping bucket precipitation gauge
Thermocouple soil temperature sensors
Campbell CS650 soil moisture probes

## Slide 9
NICE Net webpage
http://nicenet.dri.edu/
Data available in the standard WRCC format
10-minute, hourly, daily, and monthly available
All Ref ET variables: temperature, wind, humidity, solar radiation, and pre-computed ASCE grass Ref ET

## Slide 10
Weather Data QA/QC
QAQC of solar radiation, temperature, humidity, and windspeed is REQUIRED prior to comparing estimated ETo to measured ETo
Example of QAQC process of solar radiation
Based adjustments on ratios between theoretical clear sky solar radiation and top percentiles of measured data

## Slide 11
Weather Data QA/QC
Snake Valley NICE Net
Matlab QA/QC interface
Currently, only raw NICE
Net data available on web
Need to develop
automated process to put
QA/QC data back on web
Use ASCE RSOb to
compute clear sky curve
Solar bias exists in most censors, and needs some adjustment before computing ETo

## Slide 12
Arid bias is ETo estimates, NICE Net case study
Snake Valley NICE Net
Salt Desert Shrub Nevada Climate-ecohydrological Assessment Network (NevCAN)
3.5 km apart
5 m elevation difference

## Slide 13
Arid bias is ETo estimates, NICE Net case study
NevCAN
Area surrounding NevCAN
Area surrounding NICE Net
NICE Net

## Slide 14
Arid bias is ETo estimates, NICE Net case study
Arid site: larger dew point depression, lower humidity, higher temperatures, higher wind speed
[Dunkerly et al. 2014]

## Slide 15
Arid bias is ETo estimates, NICE Net case study
Annual average ETr 31% higher at arid station!
These biases must be considered in spatial ETo/ETr estimates from gridded weather data and remote sensing
[Dunkerly et al. 2014]

## Slide 16
ETo gridded weather data bias
Carson Valley NICE Net (blue line) and gridMET 4-km cell (red line)
Consistent high bias in gridMET
gridMET knows nothing about irrigation, similar to arid NevCAN station

## Slide 17
ETo gridded weather data bias correction
Boulder Valley weather station, northern NV
Make mean monthly ratios: observed/estimated
Adjust gridded data by month using ratios
Rick Allen and others working on boundary layer conditioning
[Huntington et al. 2014]

## Slide 18
ETo tools: Climate Engine

## Slide 19
ETo tools: Climate Engine
Climate Engine: easily accessible real-time gridded ETo and ET products
Application: http://clim-engine.appspot.com/
Landing page: http://climateengine.org/
Average annual ETo
gridMET
1981-2010 climatology
90-day ETo anomaly
gridMET
5-21-2016 to 8-18-2016

## Slide 20
ETo tools: Climate Engine
Near real-time ETo timeseries near Fallon, NV
May 21 though August 18, 2016
Recall high ETo biases, not representative of actual ag conditions!

## Slide 21
ETo as a drought metric
Figure 1 from Hobbins et al. 2016: Idealized parallel and complementary responses of ET and ETo to varying moisture and energy conditions shown within the Budyko framework.
Flash drought, moisture changes lag behind changes in meteorological drivers. Both ETo and ET will increase
Sustained drought, ET declines and ETo increases in response to an increasingly limited moisture supply
ETo will increase under both drought types!

## Slide 22
The Evaporative Demand Drought Index (EDDI)
Pair of papers in Journal of Hydrometeorology
Hobbins et al. 2016: EDDI theory and formulation
McEvoy et al. 2016: EDDI assessment against other drought indices
EDDI represents standardized anomalies in ETo
Based on gridMET 4-km daily data, 1979-present
+ EDDI = drought or drought development likely
- EDDI = cool and moist conditions
48-month EDDI shows excessive accumulated ETo
over the first 4 water years of CA drought

## Slide 23
The Evaporative Demand Drought Index (EDDI)
Experimental EDDI maps:
https://mydrive.dri.edu/index.php/s/XgGuJ2CKJ3sa3L6 (4-km gridMET)
ftp://ftp.cdc.noaa.gov/pub/Public/mhobbins/EDDI/USDM/ (12-km NLDAS)
ftp://ftp.cdc.noaa.gov/pub/Public/mhobbins/EDDI/CN_DEWS/ (CA/NV region)
14-day EDDI
8-17-2016
30-day EDDI
8-17-2016
180-day EDDI
(6-month)
8-17-2016
365-day EDDI
(12-month)
8-17-2016

## Slide 24
The Evaporative Demand Drought Index (EDDI)
EDDI animation slider tool: https://eddi-dri.appspot.com/

## Slide 25
Seasonal drought forecasts using ETo
McEvoy et al. 2016, GRL: Improved seasonal drought forecasts using reference evapotranspiration anomalies: http://www.dri.edu/images/stories/divisions/das/dasfaculty/McEvoy_et_al-2016-Geophysical_Research_Letters.pdf
Retrospective skill analysis using Climate Forecast System Version 2 (CFSv2) seasonal forecast model
ETo forecast skill superior to precipitation during droughts
Major improvement in central and northeast US during growing season
Minor improvement in west (CA/NV)

## Slide 26
Future directions
Continue to seek out funding opportunities to maintain NICE Net (funding ran out December 2015)! DRI and NV Division of Water Resources are seeking state funding/legislative approval for NICE Net
$2000-$3000 per station/per year (~$54K per year total)
Look forward to collaborating with Reclamation on ingesting NICE Net data for calculating well irrigated crop ET (ETo * Kc)
Integration of NICE Net into an irrigation scheduler (i.e., WA State University, Troy Peters)
Host raw and QA/QCed data on NICE Net
Develop a CONUS-wide benchmark dataset of ag stations with good, long-term records that measure ETo variables to validate gridded ETo
Further develop bias correction methodology for ETo from gridded weather data
Operationalize EDDI, 3-year NOAA funded project that just began
Produce operational bias corrected and downscaled seasonal ETo forecasts

## Slide 27
Thank you!
Dan.McEvoy@dri.edu
Justin.Huntington@dri.edu
North Spring Valley NICE Net
March, 2015