## Slide 1: NM Climate Center AgMet Network
Dave DuBois
NM State Climatologist
Las Cruces, NM
Presented at the Irrigation Management Information Systems’ Workshop
San Diego, CA, August 26, 2016

## Slide 2
The 2016 Elephant Butte (southern NM) Irrigation District allotment 13 acre-inches, 28 percent of what EBID considers to be a full allotment
This reservoir at about 7.5% capacity

## Slide 4: AgMet Network History
Started by Ken Kunkel, the first NM state climatologist in late 1980s
  Installed at NMSU Agricultural Science Centers
  Currently 12 centers state-wide
  Most collocated with NWS cooperative stations
In mid-1990s Ted Sammis created the NM Climate Center and housed hourly data at his lab for >15 years
Sammis’ network all connected through phone lines and Loggernet - dialed in after midnight each day

## Slide 5: NM Climate Center Now
Data ingested daily/hourly into MySQL database from Loggernet
Data system: Dedicated PCs on Ubuntu linux using python scripts
Public access on weather.nmsu.edu
Annual operating funds from NM
Funds from grants and contracts
Funds come from National Mesonet contract

## Slide 6: AgMet Station Map
10 active (4 in Las Cruces area)
3 permanently closed
Intend to bring 4 back online (no telemetry, being moved)
Carlsbad
Clayton
Corona
Derry area

## Slide 7
Leyendecker Plant Science Research Center, Mesilla
Pecans, chile, cover crops, alfalfa

## Slide 9
Farmington Ag Science Center
alfalfa, corn, dry beans, potatoes, onions, chile, etc.

## Slide 11
John T. Harrington Forestry Research Center at Mora
Silviculture, reforestation, etc.

## Slide 12
Fabian Garcia Science Center, Las Cruces
Chile, algae, onion, viticulture, turfgrass

## Slide 14: Basic Description: Equipment
Temperature/RH: Vaisala HMP60/50 at 2 m
Precipitation: Texas Electronics TE-525
Soil temperature: CS-107 at 10 cm
winds: Mostly MetOne 034B at 3 m
Solar radiation: Li-COR LI200X
Data loggers: mostly CR10X, few with CR1000
Telemetry: mix of 400MHz RF and telephone, one on Ethernet line
powered with 10W panel, & deep cycle battery

## Slide 15: Maintenance Schedule
Since 2010 we started collecting maintenance logs, equipment replacement logs & photos
Starting in 2010 replaced most soil temperature probes, verified sensor heights and depths
Starting in 2013 agreements with local operators assisting in maintenance and operation
Current maintenance
  Annual site visit by NMCC staff (Stan Engle, student or me)
  No calibrations
  Sensor replacements (mainly T/RH) every 3 to 4 years
  Windsets are repaired and used again

## Slide 16: QA/QC
Daily automated ingest goes through hourly value QC checks
  Looks for out of range values, missing data
  Assigns a flag if data passes this level
I look at data each day using our website to look for missing and data that looks odd
  Plot hourly data for all parameters
I relay odd behavior to Stan and local operator for next steps
Every year the NM State Engineer’s Office performs a QC on physical state of sites and checks data

## Slide 17: Path Forward
Upgrade QC and maintenance methodology
Station metadata
Funding
Partnerships
  Growers
  Across agencies

## Slide 18: NM USRCRN
Joint effort between NMSU and Park Service
Handover ownerships in 2014-2015
16 total
5 NPS

## Slide 20: Recent efforts in et
National Weather Service FRET product
  Started in Albuquerque office providing us ET at Ag Science Centers in their CWA

## Slide 21
Uses P-M from ASCE-EWRI, 2004

## Slide 22: Some quick FRET comparisons
Los Lunas Ag Science Center 2013-2014

## Slide 23
http://digital.weather.gov/

## Slide 24
http://nmclimate.nmsu.edu/evapotr/

## Slide 25
http://www.xericenter.com/

## Slide 26: Dr. Dave DuBois State Climatologist New Mexico State Univ.
dwdubois@nmsu.edu weather.nmsu.edu @nmclimate